## Slide 1: Advanced Shared Processors
Notes: Instructor Notes:
Purpose —
Details —
Additional Information —
Transition Statement —

## Slide 2: Unit Objectives
After completing this unit, you should be able to:
Explain Simultaneous Multithreading (SMT)
Understand Shared Processing Units and the effect of
Allocating excessive Virtual Processors especially in an Uncapped environment
Notes: Notes:
Here are the topics that are going to be covered in this Unit.

## Slide 3: Non partitioned Server – thread dispatch
P
P
TDQ
Operating System
LIC
Notes: Notes:
In an unpartitioned N-way iSeries system, the License Internal Code provided information on the available number of processors to OS/400. For example, for a 2-way iSeries system, the OS/400 would recognize 2 processors and dispatch (in parallel) the appropriate number of requests per processor from the Task Dispatch Queue. Naturally, the processing capacity of the system is also determined by the number of processors!
[Note: If Hardware Multi-threading (or Simultaneous Multithreading in POWER5) was supported, two tasks would be dispatched per processor. If HMT (or Simultaneous Multithreading in POWER5) was not invoked, then only one task would be dispatched per processor.]

## Slide 4: ST versus HMT versus SMT
Single Threaded
Hardware Multithreaded
Simultaneous Multithreading
time
Two tasks dispatched
Single task executed at time
One task dispatched at a time
Single task executed at time
Two tasks dispatched
Both tasks executed in parallel
OS
Task
Dispatch
Queue
Dispatched
Run
Dispatched
Run
Notes: Notes:
Singlethreaded (ST) technology dispatches only one task at a time. When this task encounters a long delay, a second task is dispatched. There is a relatively long period of processor idle time, which impacts on overall throughput of the processor.
With Hardware Multithreading (HMT), a processor could support two streams of instructions (two threads or tasks). When one task experiences a long delay resulting from a “cache miss”, the processor executes the second task’s instruction stream.
POWER5 technology supports the management of two simultaneously dispatched tasks. But with Simultaneous Multithreading (SMT) supports the two tasks execute in parallel through the “pipe” architecture. Many of the cycles or stages of the pipes not used by one thread can be utilized by concurrently executing the instruction stream of another thread.

## Slide 5: Simultaneous Multithreading - POWER5
Time (cycles)
Thread 1
Thread 2
With SMT:
Thread 1: 18% longer
Thread 2: 9% longer
69% throughput increase
... in this trivial example.
Amount of overlap is
environment dependent.
The Point
:
Capacity of system is greater.
Individual threads execute slightly slower when running concurrently.
11 cycles
11 cycles
13 cycles
12 cycles
SMT=OFF
SMT=ON
Single
Processor
Notes: Notes:
The diagrams represent a POWER5 processor. The rows represent processor “pipes”, while each processor time cycle is represented by a column. The POWER5 processor supports two load/store “pipes”, two arithmetic “pipes”, and a branch “pipe”, as well as two floating-point “pipes”.
The top diagram represents 2 instructions passing through the processor “pipes” on a POWER5 processor with Simultaneous Multithreading (SMT) turned off.
The bottom diagram depicts the same instructions Simultaneous Multithreading (SMT) turned on.
With SMT turned on the instructions are both loaded simultaneously into the processor, but they have to wait their turn for “pipe cycles” that both instructions need. This may make the total time longer for a single instruction to complete due to the possibility of contention. However, due to increased parallelism, it is more than likely that both instructions will complete in a shorted time. Thus, in a given period of time more requests can be completed, thereby increasing the overall processing capacity (throughput) of the processor.
Note: The scenario represents high utilization of the processor.

## Slide 6: Controlling Simultaneous Multithreading
SMT on POWER5 controlled by Partition Operating System
  Each OS as its own potentially different value
  I5/OS controls SMT through system value QPRCMLTTSK
    0 *OFF
      One task per physical processor
    1 *ON
      Two tasks per physical processor
    2 *System Controlled (default)
      *ON but OS may switch to *OFF
  Change takes effect at IPL of i5/OS.
Partitions allocate physical processors
  Each processor capable of running 2 threads – if SMT is on
Partitions with shared processors
  SMT mode switches with partition OS
Be aware, some servers have shipped with a value of 0. Be
sure to check that yours is 1 or 2.
Notes: Notes:
The SMT feature is controlled by the QPRCMLTTSK system value and is independently set in each partition.
When SMT is turned on, up to two threads are dispatched to each physical resulting in an environment with TWO LOGICAL PROCESSORS. With SMT turned off, only one thread is dispatched, and system will operate in an environment with ONE LOGICAL PROCESSOR. Changing the QPRCMLTTSK values requires an IPL of the partition to be activated.
When the QPRCMLTTSK is set to “System Controlled”, the system will monitor the rate of arrival of requests, and switch between the two environments to achieve optimum results.
The multitasking support on the processor (SMT on/off) will always represent the state required by the partition being serviced by the processor.

## Slide 7: Shared versus Dedicated Processors
Shared Processors
  Default state of all processors in POWER5
  Included in a Shared Processor Pool (1 pool per server)
  Processor capacity shared by multiple partitions
    Allows microprocessor partitions (partial processors allocation)
4-way system
4-processors in shared pool
Partition-A
2 dedicated -processors
Dedicated Processors
Shared Processor Pool
2-processors in shared pool
Partition-B
1.55 shared processors
Partition-C
0.45 shared processors
Dedicated Processors
  Specific processors allocated to partition
Notes: Notes:
Logical partitions : Logical partitions allow you to distribute resources in a single system to make it function as if it were two or more independent servers. A logical partition may be one of the following types, based on the way processing capacity is allocated:
shared processor logical partition: processing units allocated from a shared processor pool.
dedicated processor logical partition: whole processors allocated for exclusive use by the partition.
Shared processor pool: Group of one or more physical processors that have their processing capacity shared by one or more logical partition. Processor capacity in this shared processor pool can be allocated to logical partitions – up to the total processing capacity in the pool. By default, all processors in a POWER5 system are included in the shared processor pool. If logical partitions are configured with dedicated processors, the capacity of the shared processor pool is reduced by the number of dedicated processors allocated.

## Slide 8: Understanding Shared Processors
Four main concepts
Shared processor pool. A processor must be in the shared processor pool (now the default) to allow Processing capacity to be shared by logical partitions.
1.00 (shared) processing is approximately equivalent in processing capacity to a single processor. (2.00 Processing Units = 2 Processors and so forth). 0.5 Processing Units is approximately ½ the capacity of a whole processor – IF configured properly
Currently POWER5 processor time is allocated in 10 millisecond time slices called Dispatch Windows.
Virtual Processor – It’s the number of processors that the operating system thinks it has to use (more in this later). It’s also the number of processors you want the partition to be able to use simultaneously.
10 milliseconds
Notes: Notes:
A previous chart introduced the concept of logical partitions with dedicated processors or shared processors.
A logical partition using processors from a shared processor pool must be assigned
processor capacity and
number of processors (virtual) the partition’s Operating System must manage.
(1) Shared Processor Pool: Group of one or more physical processors that have their processing capacity shared by one or more logical partition. Processor capacity in this shared processor pool can be allocated to logical partitions – up to the total processing capacity in the pool. By default, all processors in a POWER5 system are included in the shared processor pool. If logical partitions are configured with dedicated processors, the capacity of the shared processor pool is reduced by the number of dedicated processors allocated.
(2) Processor Capacity: A logical partition with shared processors is assigned processing capacity from the shared processor pool. For a processor to be used as a shared processor it must be in the shared processor pool. A processing capacity of 1.00 processing units is approximately equivalent capacity of one processor (a processor overhead is incurred in the management of processor capacity in the shared processor pool). Capacity is allocated to a shared processor partition with a minimum capacity of 1/10th (0.10) of a processor, and in increments of 1/100th (0.01) of a processor. (Note: A logical partition with dedicated processors is assigned particular processors by the POWER5 hypervisor.)
(3) Virtual Processors : This value determines the number of “processors” from the perspective of the Operating System of the partition (i5/OS, for example), and establishes the maximum number of concurrent tasks that are dispatched for processing from the logical partition. (In addition to this, the number of virtual processors have a impact in uncapped capacity, which will be discussed later in this section).
The reference to “virtual processors” helps to differentiate from the “real processors” in the shared processor pool which is managed by the POWER5 hypervisor. The applicable number of Virtual Processors is also the number of processors reported by the Operating System as the number of “processors”. For example, in i5/OS performance data, performance reports, WRKSYSACT command etc. the number of “processors” shown correspond to the number of “virtual processors”.
(Note: The number of virtual processors assigned to a POWER5 logical partition can exceed the number of processors in the shared processor pool.)
The default action through the HMC partition creation dialog is for the system to use the minimum necessary virtual processors to satisfy your processing units. The capacity of the partition (in processing units) is rounded up to the next higher whole number to represent the number of virtual processors. For example, for a partition with a capacity of 0.75 processing units, the number of virtual processors defaults to 1. If the capacity is 1.75 processing units, the default number of virtual processors is 2.
You can assign as many a you deem necessary as long as you satisfy the restriction that a minimum of 0.10 processing unit per virtual processor is maintained. For example, a logical partition with 0.5 processing units cannot have more than 5 virtual processors, since if 6 virtual processors were specified, the processing capacity per virtual processor would be less than a 1/10th (0.10) of a processor.
(4) Timeslice Allocation : The allocation of processor capacity (currently) is managed in intervals of 10 milliseconds (0.01 seconds). This is particularly important for micropartitioned logical partitions where the number of shared processors is less than one (For example 0.10 to 0.99 processors).

## Slide 9: Processing of a User Request
10 milliseconds
10 ms
10 ms
10 ms
10 ms
Cache
Memory
Disk
For ”a” job to run it has to
Get it’s data from DISK into
Memory, into cache and finally
into the processor .
Slowest - disk
fastest - cache
Even if the data is already in
Memory it has to be loaded into
cache to run – this takes time
a
a
a
a
10 MS dispatch window
Notes: Notes:
Before a user request can be processed, it must first get it’s instructions and data to the L1 cache (from disk, into memory (through I/O operation). L3 and L2 cache. This however is not where the overhead comes in as this is normal for any operation.

## Slide 10: Dedicated vs Shared Processors
Dedicated Processor Partitions are potentially more efficient
than Shared Processor Partitions since the latter:
Increases the possibility that jobs take may take longer to
complete, and thus
  Have to be re-dispatched and potentially reload cache, which
  Increases the chance of a cache miss and
  Reduces the chance for processor and memory affinity
All the above are affected by how you allocate your virtual
processors ( more in the next few charts !)
Notes: Notes:
The end user needs to understand that using shared processors incurs some risk of performance impact.
Using shared processors makes much more work for the Power hypervisor. First you are giving a partition some number of milliseconds less than a dedicated processor(s) get. Therefore you increase the chance that the jobs won’t have sufficient time to complete and have to go back thru the dispatch/memory/cache processor routine. You increase the chance that a jobs data is no longer in cache (or even memory) and will have to be reloaded (if it’s still in memory). You increase the chance that the job, when re-run will run on a difference processor (processor affinity). You are also greatly increasing the chance that memory affinity will be impacted.

## Slide 11: Time Slice (10 Milliseconds)
10 milliseconds
Each Processor’s use is allocated within a 10 milliseconds Cycle
A partition’s use of processor capacity is assured it’s allocation during each 10 milliseconds interval
  Example-1 (One Processor Pool):
    0.80 Processing Units (80% of ONE processors time ) will be assured of up to 8 milliseconds of processing time out of each 10 milliseconds time slice. It should yield approximately 0.8 * CPW per processor.
        Every 10 milliseconds this ‘cycle’ repeats itself
10 milliseconds
10 milliseconds
10 milliseconds
  Example-2 (Four Processor Pool):
    1.80 Processing Units will be assured of up to 18 milliseconds of processing time out of each 10 milliseconds time slice. It should yield approximately 1.8 * CPW per processor.
        Every 10 milliseconds this ‘cycle’ repeats itself
10 milliseconds
10 milliseconds
10 milliseconds
10 milliseconds
10 milliseconds
10 milliseconds
10 milliseconds
10 milliseconds
18ms
18ms
9ms
5ms
6ms
6ms
6ms
2ms
1
1
2
3
4
Notes: Notes:
The iSeries POWER5-based processors (and all iSeries processors for that matter) currently work on a 10 milliseconds clock cycle. If you have a shared processor pool with 4 processors, for every 10 milliseconds on the wall clock, you would have 40 milliseconds of processing capacity.
Consider the example of 1 processor in the shared processor pool:
when 0.80 Processing units is allocated to a partition, the partition is allowed up to 8 milliseconds of processing time for every 10 milliseconds of elapsed clock time (out of a shared processor pool capacity of 10 milliseconds). Once the partition uses the allotted 8 milliseconds, it will have to wait until the next 10 milliseconds interval. In the next 10 milliseconds interval, the partition could again use up to a further 8 milliseconds. To receive this 8 milliseconds of processor capacity, the partition must have at least 1 virtual processor. However, you could have a maximum of 8 virtual processors (0.80 processor units/8 virtual processors = 0.10 processing units per virtual processors).
Consider the example of 4 processor in the shared processor pool:
When 1.80 Processing units is allocated to a partition, the partition is allowed up to 18 milliseconds of processing time for every 10 milliseconds of elapsed clock time (out of a shared processor pool capacity of 40 milliseconds). Once the partition uses the allotted 18 milliseconds, it will have to wait until the next 10 milliseconds interval. In the next 10 milliseconds interval, the partition could again use up to a further 18 milliseconds. To receive this 18 milliseconds of processor capacity, the partition must have at least 2 virtual processors. However, you could have a maximum of 18 virtual processors (1.80 processor units/18 virtual processors = 0.10 processing units per virtual processors).
When you allocate shared processing units to a partition what you are – in essence – doing is giving it some number of milliseconds of processing time. For every 10 milliseconds on the wall clock each physical processor is capable of 10milliseconds of processing time. When you see a uni-processor that’s (for example) 75% busy it means for that 10milliseconds time slice it was busy 7.5milliseconds
So if you allocate 2.50 processing units to a partition you are giving it 25milliseconds of processing time for every 10milliseconds on the wall clock, but would need to have at least 3 processors in the shared processor pool. Since the numbers of processors in the shared pool is (which now is) a floating number you may not always be able to allocate this many milliseconds. But as long as the Power hypervisor can allocate the minimum amount you specify (more on this amount later) the partition can still come active
In Power5, the processors are by default in the shared pool unless a dedicated processor partition is active OR is not active AND does NOT allow it’s idle processor(s) to be shared. Allowing inactive processors to go back to the shared pool is the default.

## Slide 12: Virtual Processors
6 processors * 10ms
= 60 milliseconds
For every 10 milliseconds of wall clock time, each processor in the shared pool is capable of 10 milliseconds of processing time
If you give a partition 0.5 processing units, it is assured up to 5 milliseconds of processing time in a 10 millisecond interval.
You have ABSOLUTELY no
control over which pool processors your jobs run on.
However, you CAN control the number of processors that the partition can utilize simultaneously via Virtual Processors
Notes: Notes:
You not only have to tell a partition how many milliseconds of processor time is assured for its use (processor capacity), but you have to tell it how many tasks it can run in parallel (virtual processors). These parameter are defined in the partition profile configuration.
New with Power hypervisor is the ability to run multiple virtual processors on a single physical processor. This means that a 1-Way (uniprocessor) system can report into the Operating System as an N-way environment.

## Slide 13: Capped versus Uncapped
  Shared Processor Pool Partitions ONLY
  (Capacity of Dedicated Processor partitions is limited by the number of dedicated processors.)
Capped (Only option up to V5R2/POWER4)
  Processing capacity is limited by the entitled capacity
    The entitled capacity is assured (.75 Processing Units = 7.5 MS)
    Partition CANNOT use any unused capacity in the processor pool
    Maximum Utilization is 100%
Uncapped
  Processing capacity may exceed the entitled capacity
    The entitled capacity is assured
    Partition CAN use unused capacity in the processor pool
    Processor Utilization may exceed 100%
      Utilization is based on entitled capacity
    Upper limit of utilization determined by VIRTUAL PROCESSORS
      (more on this later!)
    Weight
      Determines ratio of allocation of unused capacity – when more than one partition requests unused capacity. Be careful here, a weight of zero is actually a capped partition.
Notes: Notes:
Shared processor logical partition: Logical partition that uses processor capacity from the shared processor pool. The processing capacity of a shared processor logical partition is allocated in units of 0.01 (1/100th) of a processor with a minimum of 0.10 (1/10th) processors per partition from the shared processor pool. A shared processor logical partition can be assigned one of two modes:
(1) Capped: Limits the processing capacity of a shared processor logical partition to the amount of shared processing units configured. Thus, a very busy partition in capped mode cannot use additional processor capacity even if there is unused processor capacity in the shared processor pool. The number of virtual processors assigned to the partition determines the number of concurrent tasks that could be dispatched. Only capped mode logical partitions were supported in V5R2.
(2) Uncapped: Allows a shared processor logical partition to utilize processor capacity in excess of it’s configured (assured) processor capacity, provided there is unused capacity in the shared processor pool. This capability is available with V5R3 and is supported (today) on POWER5 only. The processor capacity and the number of virtual processors is allocated as in the capped mode, but the number of virtual processors also determines the upper limit of processor capacity that can be used by the partition. As of i5/OS, and POWER5-based servers, it is now possible, by using the uncapped mode, to use more capacity than is allocated to a partition, provided there is unused capacity in the shared processor pool. A partition running in uncapped mode can use unused pool processing capacity that previously (V5R2 and before) would have gone unused.
Uncapped (partition) weight: Partitions configured as uncapped also require to be assign a values which determines the amount of available capacity in the shared processor pool that will be allocated to the partition in situations when more than one partition is competing for the available capacity. This value defaults to 128 and can be between 0 and 255.

## Slide 14
Partition dog tasks a, b…. allocated 0.6 Processing Units
Partition cat tasks 1, 2…. allocated 0.4 Processing Units
a
1
b
a
10 milliseconds
10 ms
10 ms
10 ms
1
1
1
b
b
1
Example: Shared Processor - Capped
cache
(0)
(1)
(2)
(3)
4ms
4ms
4ms
4ms
3ms
4ms
1ms
Notes: Notes:
Very simplified example of 2 partitions Dog (.6 Processing Units) and Cat, (.4 Processing Units) sharing a single processor and running VERY C.P.U. intensive jobs.
Very unrealistic scenario. Example to show concepts of how capped partitions work.
Dog’s jobs are a,b,c etc
Cat’s jobs are 1,2,3 etc
Job a from partition Dog is ready to run. The Hypervisor assigns the job to run on the processor and it’s instructions and data are loaded into cache. It begins to run and:
Runs for 4 milliseconds and completes. Partition cat , has job 1 ready to run, the Hypervisor assigns it to the to the processor where it runs for 4 milliseconds. Even though there are 2 MS left in the dispatch window, it has to stop because Cat has only .4 processing units (4milliseconds) allocated to it.
At the next 10 milliseconds intersection (1) job 1 resumes running but again has to stop after CATs allotted 4 milliseconds
At the next 10 milliseconds intersection (2) job 1 resumes running but again has to stop after it’s allotted 4 milliseconds, 4 milliseconds later another of DOGs jobs (b) is ready to run and the Hypervisor assigns it to the processor. Bs data and instructions are loaded into cache and it begins to run on the idle processor. It runs to the next ‘intersection’ (3).
B continues to run at the start of intersection, (3) runs for 3 milliseconds and completes. Job 1 gets re-dispatched to the processor and starts running, runs for it’s allotted 4 milliseconds and waits.

## Slide 15
Partition dog jobs a, b….. Allocated 0.6 Processing Units
Partition cat jobs 1, 2…. allocated 0.4 Processing Units
a
1
b
a
10 milliseconds
10 ms
10 ms
10 ms
1
1
1
b
1
Example: Shared Processor - Uncapped
cache
1
1
1
1
(0)
(1)
(2)
(3)
4ms
4ms
4ms
4ms
4ms
6ms
1ms
2ms
6ms
5ms
Notes: Notes:
Simplified example of 2 partitions running VERY CPU intensive jobs.
Dog (0.6 Processing Units) and
Cat, (0.4 Processing Units)
sharing a single processor - both partitions are uncapped.
Very unrealistic scenario. Example to show concepts only.
Dog’s jobs are a,b,c etc
Cat’s jobs are 1,2,3 etc
Simple example of 2 partitions sharing a single processor
Job a from partition Dog is ready to run. The Hypervisor assigns the job to run on the processor and it’s instructions and data are loaded into cache. It begins to run and:
Runs for 4 milliseconds and completes. Partition cat , has job 1 ready to run, the Hypervisor assigns it to the processor where it runs for 4 milliseconds. Only now since partition CAT is uncapped AND there is excess unused capacity, the job can continue to run past CATs allotted 4 MS.
At the next 10 milliseconds intersection (1) job 1 can continue to run past its assured 4 MS and use excess unused capacity, it continues to do so until DOG has another job ready to run. Since CAT has already used it’s allotted 4 MS, ANY other partitions jobs will supersede it and the Hypervisor will immediately assign it to the processor.
Job B runs for 5 MS and completes. Since there is excess unused capacity in this window, job 1 is reassigned to the processor where it continues to run.

## Slide 16
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
4 Processors in the pool = 4.00 Processing Units = 40 MS Processing Time
Shared Processor Pool
Notes: Notes:
For each 10MS of physical (wall clock) time you have 40MS of processing time since there are 4 processors in the shared pool. Since we can work in 1/100th of a processor (.25 Pus) there really is not a pool of 40MS but a pool of 400Micro seconds. But for illustrative purposes we will assume our customer only works in tenths.

## Slide 17
Correct Values to enter?
It’s as IF the Hypervisor looks at the shared
Pool as no more than a Pool of time.
As far as:
Processing Units (PU):
Min = at least .10 & not greater than
number of pool/system processors
Max = at least equal to min &
no greater than the number
of processors physically
on system
Desired = between Min/Max
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
Virtual Processors:
VP number at least large enough to satisfy
corresponding (desired/min/max) PU value
VP number no greater than 10 times
corresponding PU value
Desired is not less than Min VP &
no greater than Max VP
Notes: Notes:
The above is really more in line with what really happens. As far as the HMC is concerned 4 processors in the pool represents a pool of 40MS. When you configure a partition with shared processors it allocates some number of MS from this pool. It really doesn’t care how many processors are in the pool, you tell the OS how many processors the partition will have via the Virtual Processor field.
All the Hypervisor really cares about is:
1. The minimum processing Units is at least .10
2. The maximum processing units is no greater than the number of processors physically on the system
3. Is the desired processing units at least equal to or greater than the min AND at least equal to or less than the Maximum
4. Is the number of virtual processors sufficient to cover the Processing Units (min/desired/max)
5. Is the number of virtual processors no greater than 10 times the number of Processing Units (min/desired/max)
6. Is the desired number between the min and the max
You are responsible for the optimum setting of these values.

## Slide 18: Point of Confusion
What does this really mean?
That the number of Virtual Processors only needs to be large enough to satisfy the
corresponding (desired/minimum/maximum) number of Processing Units. 1.5 PUs
has to have to have at least 2 Virtual Processors but could have up to 15 (1.5 X 10
= 15) Virtual Processors. SHOULD is a totally different issue.
What it doesn’t mean is that the number of desired Virtual processors HAS (or
should for that matter) to be 10 times the number of Desired Processing Units
Remember, the OS sees the number of Virtual Processors, that you assign to a
partition, as the number of Physical processors it has to work with.
Notes: Notes:
This is where I think a lot of people are getting themselves into trouble. They see this statement – replicated several time – and assume it means the corresponding virtual number HAS to be 10 times the corresponding desired number.

## Slide 19
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
Capped example – Creating P3
P3 Max 100% (5/5) busy
1 VP = 2 threads 2 total
P3 .5 desired Processing Units and
1 Virtual Processor. The OS in P3
thinks it has 1 processor and acts
accordingly.
Notice that no 2 processors can
be in use by P3 in any one time
period.
Capped also means that P3 can’t use
any more than 5 MS – regardless
of excess capacity
More Virtual Processors only gets more
Jobs dispatched to compete for the 5 MS
P3
Notes: Notes:
What happens when you create a capped partition with .5 Pus. The Hypervisor will allocate 5 MS from the pool leaving 3.5 Pus left unallocated. Since you gave it a VP of 1 (the min whole number necessary to cover the 5 MS – which by the way is the recommended way to configure a capped partition) the OS would think it is a uni processor and act accordingly.
Since the OS thinks it’s a 1 way it can only dispatch 2 threads which can only run on 1 processor at a time – IF SMT is on.
Adding more Virtual processor only gets more threads dispatched, the partition is still limited to a total of 5MS. Then each thread would likely get even less processor time per ever 10 MS ‘cycle’.

## Slide 20
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
Uncapped examples – Creating P1
P1 Max 200% (10/5) busy
1 VP = 2 threads 2 total
P1 .5 desired Processing Units and
1 Virtual Processor. The OS in P1
thinks it has 1 processor and acts
accordingly.
Notice that no 2 processors can
be in use by P1 in any one time
period. That’s what a VP of 1
means. It also means that P1 can’t
use any more than 1 processors
worth of time (10MS) per physical 10MS
and can’t use but 1 processor simultaneously.
P1
Notes: Notes:
What happens when you create a partition with .5 Pus. The Hypervisor will allocate 5 MS from the pool leaving 3.5 Pus left unallocated. Since you gave it a VP of 1 (the min whole number necessary to cover the 5 MS) the OS would think it is a uni processor and act accordingly.
Since the OS thinks it’s a 1 way it can only dispatch 2 threads which can only run on 1 processor at a time – IF SMT is on.

## Slide 21: Virtual Processors vs Real Processors - Uncapped
Real Processors in Shared Pool (N-way)
TDQ
User
Requests
VP
2 threads
per “proc”
PARTITION - A
Processor Capacity
POWER5 Hypervisor
Request
Dispatched
Operating System
Notes: Notes:
In an unpartitioned N-way iSeries system, the License Internal Code provided information on the available number of processors to OS/400. For example, for a 2-way iSeries system, the OS/400 would recognize 2 processors and dispatch (in parallel) the appropriate number of requests per processor from the Task Dispatch Queue. Naturally, the processing capacity of the system is also determined by the number of processors!
[Note: If Hardware Multi-threading (or Simultaneous Multithreading in POWER5) was supported, two tasks would be dispatched per processor. If HMT (or Simultaneous Multithreading in POWER5) was not invoked, then only one task would be dispatched per processor.]
Similarly, in a POWER5 logical partition with shared processors, the hypervisor would ensure that the Operating System (for example, i5/OS) recognizes the number of tasks it had to dispatch in parallel.
The number of “processors” in a shared processor partition is determined by the number of Virtual Processors defined to the Hypervisor through the partition profile. This is an integer, because it represents processors.
The processing capacity of the partition is specified by the number of Processing Units the partition has at the time. The processing capacity must be greater than 1/10th (0.10) of a processor and can be specified in increments of 1/100th (0.01) of a processor.
Note: the number of Processing Units per Virtual Processor cannot be less than 0.10.
In a shared processor logical partition, the Operating System dispatches tasks to the processors it recognizes (Virtual Processors). The hypervisor dispatches the virtual processors to the real processors in the shared processor pool.
In capped mode : the amount of processor capacity assigned is limited by the allocated capacity (Processing Units).
In uncapped mode: the amount of processor capacity assigned is limited by the number of “processors” (Virtual Processors).

## Slide 22
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
P1 Max 800% (40/5) busy
5VP = 10 threads 10 total
Difference between can and shouldn't
Configure P1 to use 5 desired Virtual
processors. The OS in P1 thinks it
has 5 processor and acts accordingly.
P1 is assured 5 MS but could
possibly use all 4 processors worth of
time or all 40 MS
Notice at time period 3 all 4
processors could be used by P1
simultaneously
P1
Uncapped examples – more Virtual Processors
Notes: Notes:
Now instead of giving it 1 VP let’s give it 5 VPs (I’m still within the min/max range for VPs) and see the difference. For one the OS could run jobs/threads concurrently on all 4 processors. The partition is assured at least 5 MS from the pool but since the VP number is at least as large as the physical number in the pool it’s been ‘allowed’ to use as many MS as it can get it’s hands on.
Now the OS thinks it has 5 processors and could dispatch as many as 10 threads.

## Slide 23: Virtual Processors vs Real Processors
Real Processors in Shared Pool (N-way)
TDQ
User
Requests
2 threads per processor, 5
Processors = 10 threads
PARTITION - A
Processor Capacity
POWER5 Hypervisor
Request
Dispatched
Operating System
VP
VP
VP
VP
VP
With just a single
Partition using .5
of a processor I’m,
trying to run 10
threads on 4
processors
Notes: Notes:
Now – even though I have only one partition configured and running and it only has half a processor – I’m trying to run 10 threads on 4 “physical” processors.
The reason why you might want to do this would be to run a partition truly uncapped. In other words this partition COULD conceivably run at 800% busy. In other words running on all the processors in the pool ALL of the time. To run at a 1,000% percent you would have to give the partition (desired) .4 (or less) Pus. However, unless this partition REALLY needs that much processing capacity you are potentially going to have performance issues when the rest of the processors in the pool (and more virtual processors are added) are allocated to more partitions.

## Slide 24
P1 Max 800% (40/5) busy
5VP = 10 threads
P2 Max 133% (20/15) busy
2VP = 4 threads 14total
P2 has 1.5 Processing Units and
2 Virtual Processors. The OS in P2
thinks it has 2 processor and acts
accordingly.
P2 is assured 15 MS but could
possibly use up to 2 processors worth
of time for a total of 20MS
Notice at several time periods
2 of P2s jobs could be running
simultaneously – but only on 2 processors
P2
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
Uncapped examples – Creating P2
Notes: Notes:
Let’s create a second partition and give it 1.5 Pus desired and give it the smallest number of corresponding (desired) VPs of 2.
Now you can see 2 processors being used simultaneously. This is because I Had to give it 2 VPS since my desired real (Pus) represents 15MS and I have to give the partition at least 2 10MS ‘Virtual Processors’.

## Slide 25: Virtual Processors vs Real Processors
Real Processors in Shared Pool (N-way)
Processor Capacity
POWER5 Hypervisor
2 threads
per “proc”
7 VPs =
14 threads
4 physical
processors
Operating System
TDQ
User
Requests
PARTITION – P1
Request
Dispatched
VP
VP
VP
VP
VP
VP
VP
PARTITION – P2
User
Requests
Notes: Notes:
By adding a second partition with 2 VPs you can see where now as many as 14 threads could be dispatched because P1 thinks it has 5 processors and P2 thinks it has 2 processors. But there are still only 4 physical processors. Which Can't physically run any more than 8 threads simultaneously. .

## Slide 26
P1 Max 800% (40/5) busy
5VP = 10 threads
P2 Max 266% (40/15) busy
15VP = 30 threads 40 total
Difference between can and
really shouldn’t
The OS in P2 now thinks it has 15
processors and acts accordingly.
P2 is assured 15 MS but could
possibly use up to 4 processors
worth of time for a total of 40MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
P2
Uncapped examples – More Virtual Processors P2
Notes: Notes:
Let’s change the Virtual number to 15 (10 X 1.5). Now the OS would think it has 15 processors to work with and proceed to dispatch 30 threads.
No need to see the graphic foil since it would show 2 partitions (still only using 2.0 allocated Pus) trying to dispatch and run 40 threads.
The first plan of attack world be to use a Virtual number no greater than the physical number in the pool. Is it?

## Slide 27
P1 .5 Pus desired 4 VP = 8 threads
P2 1.5 Pus desired 4 VP 8 threads
P3 .8 Pus desired 4 VP 8 threads
P4 1.2 Pus desired 4 VP 8 threads 32 total
Let’s use no more processors
than there are processors in the
pool.
Sew, you’re trying to run 32 threads on 4 physical processors which can’t run any more than 8 simultaneously, resulting in:
Each thread getting less time to run per cycle of time
Increasing the likelihood that the job will take longer to complete and
Have to be re dispatched and when it does
It might run on a different processor, cache will have to be reloaded or
Even if it runs on the same processor, cache might still have to reloaded
ALL of which can adversely affect performance
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
1MS
Uncapped examples
Notes: Notes:
We can see from the foil that even setting the Virtual number no greater than the physical number in the pool can still potentially cause performance issues. Since each partition’s OS thinks it has 4 processors it’s possible that there are now 32 threads wanting to run on a Server where the Hypervisor can only handle 8 virtual processors/threads simultaneously. And here we are only dealing with 4 partitions.
A extreme example would be 40 partitions each with .10 Pus and 1 VP each. You could have 80 threads wanting to run on 4 physical processors.

## Slide 28
There is no good reason to ever have the current (desired) Virtual Processor
number greater than the number of processors in the Shared Pool or the Maximum
Virtual Processor number greater than the physical number of processors.
Understand that .5 PUs is NOT in reality 1/2 of the CPWs of a single processor,
especially if configured with the desired number of Virtual Processors
set to high – like 5 VPs for a Managed System with only 2 Pool Processors.
Consider using Dedicated Processors if the required Processing Units is close to
a whole number.
Do you really want a partition running at 1,000% ? Almost ANY partition running
consistently over 100% is undersized as far as (real) Processing Units goes.
Keep the desired number of VPs low, but set your Maximum number of VPs
high enough so that the few times you might really want to run uncapped
(end of month/year) and use excess capacity, you can raise the desired VP #
w/o having to de/reactivate the partition.
Understand that any uncapped partition running consistently over 100% busy is
using resources not currently in use. In the future these ‘excess’ resources may
well not be there.
Net it out
Notes: Notes:
Foil is self explanatory.

## Slide 29: Dedicated or Shared (Capped or Uncapped)?
The best performance may be achieved by using Dedicated processors. However Dedicated Processors partitions cannot use capacity unused by other partitions, nor can uncapped shared processor partitions utilize unused dedicated capacity.
For Shared Processors partitions (both capped and uncapped), setting Virtual Processor number too high may degrade performance.
Uncapped Shared Processor partitions can use excess capacity of the processors in the shared pool. Setting Virtual Processors too low will limit amount of additional capacity that can be used. Setting too high may negatively impact performance.
For uncapped partitions, the operating system considers the number of Virtual Processors as equal to the number of processors in the partition. You will need an OS license (i5/OS, Linux or AIX 5L) for the lesser of the number of current (desired) virtual processors or the number of processors in the shared pool.
What does IBM recommend? It depends on YOUR workload.
?
or
Notes: Notes:
(1) How do you decide on using Dedicated or Shared Processors?
(2) If you select Shared Processors, is it to be?:
Capped or
Uncapped
– and if uncapped, which weighting factor to assign it and
how many virtual processors do I allocate?

## Slide 30: Checkpoint Solutions (1 of 3)
When configuring a partition profile to use shared processors, if you give it 0.75 Processing Units and 5 Virtual Processors, what are you specifying?
a. You have to keep at least 5 processors in the shared processor pool
b. You have the ability to run up to 10 concurrent jobs/threads simultaneously – depending on the QPRCMLTTSK value
c. 5 of the processors in the pool are reserved for your use only
d. You can’t have any more than 5 processors in the pool at any given time
2. The most efficient use of processing resources is accomplished by using?
a. All partition use shared processors
b. All Partitions use dedicated processors
c. Some use shared, some use dedicated
d. It depends - on the workload
3. A difference between capped and uncapped partitions is?
a. Uncapped allows you to access all un-utilized processing resources
b. Capped is more efficient
c. Applications run faster uncapped
d. None of the above
Notes: Notes:

## Slide 31: Checkpoint Solutions (1 of 3)
When configuring a partition profile to use shared processors, if you give it 0.75 Processing Units and 5 Virtual Processors, what are you specifying?
a. You have to keep at least 5 processors in the shared processor pool
b. You have the ability to run up to 10 concurrent jobs/threads simultaneously – depending on the QPRCMLTTSK value
c. 5 of the processors in the pool are reserved for your use only
d. You can’t have any more than 5 processors in the pool at any given time
2. The most efficient use of processing resources is accomplished by using?
a. All partition use shared processors
b. All Partitions use dedicated processors
c. Some use shared, some use dedicated
d. It depends - on the workload
3. A difference between capped and uncapped partitions is?
a. Uncapped allows you to access all un-utilized processing resources
The partition could be “partially” capped, .80 Processing units and 1 Virtual
processor CAN’T use any more than 10 MS – even if there are more than
10 MS of unused capacity.
b. Capped is more efficient – it depends on the application.
c. Applications run faster uncapped – again it depends on the application
d. None of the above
Notes: Notes:

## Slide 32: Checkpoint (2 of 3)
4. You create a partition with 2.5 Processing Units, what is the minimum number of virtual processors it must have?
a. 1
b. 2
c. 3
d. It depends
5. What is the maximum number of Virtual processors possible with 2.5 Processing units?
a. 1
b. 2
c. 3
d. 25
e. 64
f. There is NO maximum
6. Which is the better idea – assuming you have 4 processors in the shared pool?
a. 3
b. 25
Notes: Notes:

## Slide 33: Checkpoint (2 of 3)
4. You create a partition with 2.5 Processing Units, what is the minimum number of virtual processors it must have?
a. 1
b. 2
c. 3
d. It depends
5. What is the maximum number of Virtual processors possible with 2.5 Processing units?
a. 1
b. 2
c. 3
d. 25
e. 64
f. There is NO maximum
6. Which is the better idea – assuming you have 4 processors in the shared pool?
a. 3
b. 25
Notes: Notes:

## Slide 34: Checkpoint (3 of 3)
7. What does IBM recommend for the use of capped/uncapped mode to achieve the most efficient use of processing resources?
a. dedicated
b. Shared Capped
c. Shared Uncapped
d. None of the above
8. Back to question number 1. If there were only 4 processors in the shared pool would it do you any good to set the Virtual Processor number at 5?
a. Yes
b. No
c. It depends
9. Back to question 8, IF you set it at 5 – or greater – could this
adversely affect system performance?
a. Yes
B. No
Notes: Notes:

## Slide 35: Checkpoint (3 of 3)
7. What does IBM recommend for the use of capped/uncapped mode to achieve the most efficient use of processing resources?
a. dedicated
b. Shared Capped
c. Shared Uncapped
d. None of the above We can’t. It’s too workload dependant. However using uncapped can provide for more system utilization, greater throughput for many workloads, potentially lower response times for workload with spikes in processor
8. Back to question number 1. If there were only 4 processors in the shared pool would it do you any good to set the Virtual Processor number at 5?
a. Yes
b. No
c. It depends
9. Back to question 8, IF you set it at 5 – or greater – could this
adversely affect system performance?
a. Yes
b. No
Notes: Notes:

## Slide 36: Unit Summary
Having completed this unit, you should be able to:
Explain/understand:
Simultaneous Multithreading (SMT)
Shared Processing Units and the effect of
Allocating excessive Virtual Processors especially in an Uncapped environment
Notes: Notes: