## Slide 1: Chapter 3
Hardware Systems and LPARs
60
Animation
(Use Slideshow)

## Slide 2: Objectives
In this chapter you will learn:
  About Mainframe hardware design
  About processing units and disk hardware
  About some typical hardware configurations

## Slide 3: Introduction
Here we look at the hardware in a complete system although the emphasis is on the processor “box”
Terminology is not straightforward
  Ever since “boxes” became multi-engined, the terms system, processor, and CPU have become muddled

## Slide 4
“Processors”
“CPUs”
“Engines”
“PUs”
“CPs”
(IFLs, ICFs, SAPs,
zAAPs, zIIPs,
spares)
“Box”
“CEC”
“CPC”
“CPU”
“Machine”
“Processor”
“Sysplex”
“System”
Note: LPAR may be referred to as an “image” or “server”
Heritage Terminology

## Slide 5
Logical Partitioning Mode (LPAR)
X
“Only” operates in
Processor System /
Resource Manager
Hipervisor
CPUs
Storage
I/O Config.
are
partitioned
Mainframe
Notes: Among the system control function is the ability to partition the system into logical partitions (LPARs)
Initial limit was 15 LPARs but newer machines (EC) allow 60 partitions
Practical considerations can limit the number to less than this as each LPAR needs memory, I/O, and processing power

## Slide 6: System Z Logical Partitioning
LPAR – Ability to define independent logical OS images
Up to
60 LPARS
Partition 1
Partition 2
Partition 3
Partition 4
Partition 5
Partition 6
Partition 7
Partition 8
Partition 9
Partition 10
Partition 11
Partition 12
Partition n
Partition n
Partition n
Partition n
Keep on practical side of resource requirements on LPAR numbers
Notes: 1. LPARs are the equivalent of a separate mainframe for most practical purposes
a. Each LPAR runs its own operating system
b. Each LPAR is independent
2. Devices can be shared across several LPARs
3. Processors can be dedicated or shared
a. each LPAR is assigned a number of logical processors (up to the maximum number of physical processors)
b. and a assigned a relative weighting

## Slide 7
zVM
v4.2
z/OS
V1.7
z/OS
V1.6
z/OS
V1.8
VSE
V3.1
L
I
N
U
X
VSE
V3.2
z/OS
V1.7
z/OS
V1.5
VSE
V3.2
L
I
N
U
X
L
I
N
U
X
zVM
v4.4
***
z/OS
V1.8
Partitioning allows for different OS’ and their Releases
15 – 60 LPARs
Hypervisor
At LPAR creation time each partition is given a weight
The weight is used to differentiate workload importance
Processor Resource / System Manager

## Slide 8
CP
Logical CP
CP
CP
CP
CP
CP
CP
CP
CP
LPAR1 LPAR2 LPAR3 LPAR4 LPAR5
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
Logical CP
CP
Dedicated
Physical
Engines
Shared
Physical
Engines
illustration
5 LPARS
10 CPs
Processors in an LPAR
Notes: System administrators assign:
  Memory
  Processors
  CHPIDs either dedicated or shared
This is done partly in the IOCDS and partly in a system profile on the Support Element (SE) in the CEC. This is normally updated through the HMC.
Changing the system profile and IOCDS will usually require a power-on reset (POR) but some changes are dynamic

## Slide 9
System z
LPAR 3
LPAR 2
LPAR 1
Processor Resource / System Manager (PR/SM)
Websphere
(SOA)
Traditional
OLTP and
Batch
Linux
LPAR CPU Weight Management can change dynamically
Move resources to
where workload is …
More
Workload
Demand !
pu
pu
pu
pu
pu
pu
pu
No operator intervention
I R D

## Slide 10: z10 Implementation “54-WAY Mainframe”
54 way SMP
336 Power PC processors to control Ficon
I/O DEVICE DRIVERS
OPERATING SYSTEM &
PLUS 10 MORE
APPLICATION CODE
& SOME OS and Crypto
SYSTEM RESOURCE MGT
Processors (Engines)
Java Apps
zAAPs
DB Apps
zIIPs
Linux
I F Ls
SAPs
ICFs
illustration

## Slide 11
Channels

## Slide 12: Current design
Current CEC designs are considerably more complex then the early S/360 design
This new complexity includes
  I/O connectivity
  I/O operation
  Partitioning of the system

## Slide 13: Enterprise Connectivity (ESCON)
In 1990, ESCON has replaced the parallel channel as being the main channel protocol for I/O connectivity, using fiber optic cables and a “switched” technology for data traffic.
Notes: Again….IBM parallel channel technology was introduced in 1964 and served Large Scale Computing Enterprises as the sole channel architecture until 1990, when Enterprise Systems
Connection (ESCON) Architecture was announced. At that time, substantial investment in
parallel channel devices, such as printers, display controllers, and tapes, were protected by
Parallel-to-ESCON converters that enabled installations to avail themselves of the improved
ESCON channel characteristics such as distance, bandwidth, and elimination of bus and tag
cable bulk.
ESCON was an integral part of the Enterprise Systems Architecture/390® (ESA/390) and, by
extension, of the z/Architecture. ESCON replaces the previous S/370 parallel OEMI with the
ESCON I/O interface, supporting additional media and interface protocols. By replacing the
previous bus and tag cables and their multiple data and control lines, ESCON provides
half-duplex serial bit transmission, in which the communication protocol is implemented
through sequences of special control characters and through formatted frames of characters.
In contrast to the previous copper cables used in the parallel OEMI, ESCON utilizes fiber
optic cables for data transmission. These cables are 100 times lighter than the old bus and
tag cables, have substantially reduced bulk, have no electrical pins, have a smaller and more
reliable connector, have reduced loss and distortion, and are free from parallel signal skew.
----------------------------------------------------------------------------
24444- Since 1990, ESCON has replaced the parallel channel as being the main channel protocol for
I/O connectivity, using fiber optic cables and a “switched” technology for data traffic.
ESCON is an integral part of z/Architecture™ for System z9 and zSeries servers, augmenting
the previous S/370 parallel Original Equipment Manufacturer’s Information (OEMI) interface.
Unlike the previous bus and tag cables and their multiple data and control lines, ESCON
provides bi-directional serial bit transmission, in which the communication protocol is
implemented through sequences of special control characters and through formatted frames
of characters.
In contrast to the previous copper cables used in the parallel OEMI, ESCON utilizes fiber
optic cables for data transmission. These cables are 100 times lighter than the old bus and
tag cables, have substantially reduced bulk, have less loss and distortion, and are free from
relative signal skew.
The ESCON link data rate is 200 megabits per second (Mbps) which results in a maximum
aggregate data rate of up to 17 megabytes per second (MB/s).The maximum unrepeated
distance of an ESCON link using multimode fiber optic cables is 3 km (1.87 miles) when using
62.5 micron fiber.
These ESCON link distances can be extended using a variety of solutions.

## Slide 14
FICON
Fibre Connection

## Slide 15: Advantages of FICON over ESCON
FICON improves distance solutions by a factor of 10.
– ESCON data droop is significant at 9 km.
– FICON has negligible data droop up to 100 km.
FICON provides up to twenty times greater bandwidth per channel.
– Maximum ESCON data rate is 17 MB/s (20 MB/s link data rate).
– Maximum FICON data rate is > 340 MB/s (400 MB/s link data rate).
FICON supports 16 times as many devices.
– ESCON supports 1 K unit addresses per channel.
– FICON supports 16 K unit addresses per channel.
FICON uses fiber more efficiently.
– ESCON has half-duplex data transfer.
– FICON has full-duplex data transfer.
FICON provides greater configuration flexibility.
– ESCON is circuit-switched. There are restrictions on large and small block intermixing.
– FICON is packet-switched. There are no restrictions on large & small block intermixing.
FICON provides relief for “channel constrained” systems.
– FICON delivers up to 2688 ESCON equivalent channels on z9 EC, with the maximum
number of 336 FICON channels (448MHz).
– FICON can span LCSSs, while ESCON can only be shared within a CSS.
Additional FICON advantages include:
- Protection of customer’s ESCON control unit investments, reducing cable bulk and
extending the maximum distance.
- Reduced IOQ (I/O queue time).
- More Parallel Access Volumes (PAV) possibilities as FICON supports attachment of up to
16384 devices, reducing the time to wait at a device (UCB).
- Reduced controller global PENDing times.
reference

## Slide 16
Open Systems Adapter (OSA)
= OSA

## Slide 17
Why MIF Channels example
Channel Sharing
Multi Image Facility

## Slide 18
Channel Subsystem Connectivity
The CHPIDs map to
physical channel ports
on the server
The channel ports
attach to the director ports,
then to control units
that subsequently attach
to the I/O devices
High data rate
Switches
Note: A large
Switch may have
200 connections
all passing data at
the same time !
STATUS
CHPID = Channel Path Identity

## Slide 19: I/O Connectivity Summary continued…
I/O control layer uses a control file IOCDS that translates physical I/O addresses into devices numbers that are used by z/OS
Device numbers are assigned by the system programmer when creating the IODF and IOCDS and are arbitrary (but not random!)
On modern machines they are three or four hex digits

## Slide 20
Hardware is configured via HMC
Support
Elements

## Slide 21
System Element (via HMC)
Locate CSS

## Slide 22: 2105 Enterprise Storage Server (ESS)
Emulates a large number of control units and 3390 disks. It can also be partitioned and connect to UNIX and other systems as SCSI devices.
There are 11 TB of disk space up to 32 channel interfaces, 16GB cache and 284MB of non-volatile memory

## Slide 23: Parallel Access Volumes (PAVs)
Alias Address
Alias Address
Base Address
Alias Address
Workload Managed
*A bitmap is maintained with
each PAV device indicating
the service class used
* High contention devices will
be identified having a
significant amount of IOSQ.
UCB identifies a device
ESS is Enterprise Storage System
IOSQ identifies device queuing for an I/O
UCB
100
Striping is available
across multiple physical
disks - i.e. DB2 TABLESPACEs
PAVs enable a single attaching System z server to simultaneously process
multiple I/O operations to the same logical volume
This is achieved by defining multiple address aliases per volume
ESS provides WLM with sophisticated ways to control I/O across a sysplex
Creating PAVs can significantly reduce device queue delays improving throughput
and I/O response times
z/OS can exploit dynamic PAV tuning using WLM
- WLM monitors the device’s performance to reassign alias addresses from one base to
another when SLOs are not being met.

## Slide 24
Multiple Allegiance (MA)
Appl. A
UCB
100
Appl. B
UCB
100
z9 z9
Multiple
Allegiance
100
Logical Volume
Physical
Disk
Drives
(Alias PAVs)
Multiple Allegiance expands the simultaneous logical volume access capability across multiple z servers
This function along with PAV enables DS8xxx Series to process more I/Os in parallel to improve performance - Reduces PEND time across LPARs

## Slide 25
Multi-Allegiance (MA) Impact illustration
This displays the potential impact on response time without/with MA operations
Implementing MA eliminates any queuing time to a device
SYS A
SYS B
I/O Op 1
I/O Op 2
START END
CONNECT
I/O Op 1
Contention
Contention
Disconnect
Re-Connect
START END
Disconnect
CONNECT
I/O Op 2
No Multi-Allegiance Support
Volume Contention
Elongated Response Time
I/O Op 1
I/O Op 2
START END
CONNECT
I/O Op 1
START END
CONNECT
I/O Op 2
Multi-Allegiance Support
Reduced I/O
Response Time
SYS A
SYS B
SYS A
SYS B

## Slide 26: Clustering
Clustering has been done for many years in several forms
  Basic shared DASD
  CTC/GRS rings
  Basic and Parallel sysplex
Image is used to describe a single z/OS system, which might be standalone or an LPAR on a large box

## Slide 27
Limited capability
Reserve and release against a whole disk
Limits access to that disk for the duration of the update
Reserve
Release

## Slide 28: CTC Ring (form of clustering)
Global Resource Sharing (GRS) used to pass information between systems via the CTC ring
Request ENQueue on a dataset, update, the DEQueue
Loosely coupled system
Every system had its own devices (no resource sharing)
2 ani
lock

## Slide 29: Hub and Spoke – NO Ring
Solution

## Slide 30: SYStems ComPLEX = SYSPLEX
z/OS
Images
z/OS
Images
z/OS
Images
z/OS
Images
z/OS
Images
z/OS
Images
z/OS
Images
z/OS
Images
z/OS
Images
What is it . . .
… A cluster
of z/OS
images
z/OS Image
Notes: - Parallel and clustered systems initially found in numerically intensive markets have gained increasing acceptance in commercial segments as well. The architectural elements of these systems span a broad spectrum that includes massively parallel processors that focus on high performance for numerically intensive workloads, and cluster operating systems that deliver high system availability.
The zSeries cluster (parallel system complex, or Parallel Sysplex) contains innovative multisystem data-sharing technology, allowing direct, concurrent read/write access to shared data from all processing nodes in the parallel configuration, without sacrificing performance or data integrity. Each node is able to concurrently cache shared data in local processor memory through hardware-assisted cluster-wide serialization and coherency controls. This in
turn enables work requests associated with a single workload, such as business transactions or database queries, to be dynamically distributed for parallel execution on nodes in the sysplex cluster, based on available processor capacity. Through this state-of-the-art cluster technology, the power of multiple z/Series systems can be harnessed to work in concert on common workloads, taking the commercial strengths of the z/OS platform to improved levels of competitive price/performance, scalable growth, and continuous availability.
Prior to Parallel Sysplex, S/390 and today zSeries customers had been forced to contain the capacity requirements of a workload within the technology limits imposed by the size of the largest single symmetric multiprocessor system available. Workload growth beyond these limits required splitting the workload and re partitioning the database between the nodes: a complex, resource-intensive process not supportive of customer business objectives.

## Slide 31: Objective is a Single System Image
From a
single
console

## Slide 32: ODI’s Initial Base Sysplex (LPAR Communication)
System
Image …n
Appl 6
Appl 3
Appl 4
System
Image 4
Appl 6
Appl 3
Appl 4
Test
Different Workloads
Test
Test
Under
Writing
System
Image 2
Appl 2
Appl 7
System
Image 3
Appl 6
Appl 3
Appl 4
Claims
Under
Writing
Under
Writing
System
Image 1
Appl 1
Appl 5
Hipersockets via TCP/IP
Coupling Facility via XCF
Notes: HACWSCC

## Slide 33: What Else a Sysplex Can Do ….
Platform for continuous availability so that applications can be available 24 hours a day, 7 days a week, 365 days a year
Ability to do more work
  Greater capacity
  Improved ability to manage response time
  Platform for further capacity and response time advances
Greater flexibility
  Ability to mix levels of hardware and software
  Ability to dynamically add systems
  An easy path for incremental growth
  Rolling application maintenance
Workload balancing
Notes: Summary of these point

## Slide 34: Parallel Sysplex Used for Resource Sharing (Eliminating Duplication)
Claims
Test
Test
Test
Under
Writing
Under
Writing
Under
Writing
System
Image 1
System
Image 2
System
Image 3
Appl 1
Appl 2
Appl 5
Appl 6
Appl 3
Appl 7
Appl 4
data
data
data
Different Workloads
Tape
Tape
Tape
Tape
Master
Console
$$$
Operations
Log
Catalog
Immediate Value
System Management Simplification
Single Image – Single Point of Control
Configuration Management Simplification
(COST CONTROL)
Elimination of redundant hardware / software components
Security
i.e. RACF
FYI - Logger is Policy
Based Management
MQ Shared
Queues
Coupling Facility
Notes: SLIDE OBJECTIVE: SET UP THE REQUIREMENT
Data Sharing
Lets look at how a shared access system works on the mainframe. We share workloads through multiple partitions and share all data through a common environment. Through the coupling facility we can share that data across multiple system images and application environments. That shared data happens because of I/O, disk devices are all shared through the integrated Channel-Architecture which has its foundation back to its original 360 design.
----- previous speaker notes -----
Connecting a large number of systems brings with it special considerations, such as how the large number of systems communicate and how they cooperate to share resources. These considerations affect the overall operation of z/OS systems. A sysplex significantly changes the way z/OS systems can share data. As the number of systems increase, it is essential to have an efficient way to share data across systems. The Coupling Facility enables centrally accessible, high-performance data sharing for authorized applications, such as subsystems and z/OS components, that are running in a sysplex. These subsystems and components then transparently extend the benefits of data sharing to their
applications. Use of the Coupling Facility substantially improves the feasibility of connecting many z/OS systems up to 32 with near linear scalability together in a sysplex to process work sharing data in parallel.
The concept of data sharing is not new. This data sharing capability follows the heritage of the mainframe’s design of share-everything architecture. Different applications within a system often need to access the same information, sometimes to read it and other times to update it. Sometimes several copies of the data exist, and with that comes the requirement of keeping all of the copies identical. If the system fails, you need a way to preserve the data with the most recent changes.
Data validity is controlled by a data management system. Within a single z/OS system, the data management system keeps track of which piece of data is being accessed or changed by which application in the system. It is the data management system’s responsibility to capture and preserve the most recent changes to the data, in case of system failure.
When two or more z/OS systems share data, each system has its own copy of a data management system. Communication between the data management systems is essential. Therefore, multisystem data sharing hinges on high-performance communication to ensure data validity among multiple data management systems, and it requires high-speed data accessing methods. Enabling the application for continuous availability gives you the opportunity to keep it running and stable even if one or more servers should become unavailable as a result of:
* Unplanned failures on one or some (but not all) of the servers
* Planned outages in the operations of one or some of the servers in connection with reconfiguration, upgrades,
maintenance
This feature of Z also provides for enhanced Total Cost of Ownership. There is little need to propagate or move data due to application locality. The Coupling Code allows for central processing of data without the concern of resource movement.
An enhancement is the System Managed Coupling Facility Duplexing which is a set of architectural extensions for Parallel Sysplex providing increase availability and access reliability for data structure redundancy.

## Slide 35: Parallel Sysplex Used for Shared Data (Workload Balancing )
* Internal License Code
LPAR1 LPAR2 LPAR3
LPARn
LPARn
Claims
Test
Test
Test
Under
Writing
Under
Writing
Under
Writing
Mainframe’s design is a share-everything architecture
The Coupling Facility* provides the technology to shared data concurrently amongst different or similar workloads
Data sharing provides for continuous availability and reliability
Different Applications
Same Applications
Notes: SLIDE OBJECTIVE:
Data Sharing
Lets look at how a shared access system works on the mainframe. We share workloads through multiple partitions and share all data through a common environment. Through the coupling facility we can share that data across multiple system images and application environments. That shared data happens because of I/O, disk devices are all shared through the integrated Channel-Architecture which has its foundation back to its original 360 design.
----- previous speaker notes -----
Connecting a large number of systems brings with it special considerations, such as how the large number of systems communicate and how they cooperate to share resources. These considerations affect the overall operation of z/OS systems. A sysplex significantly changes the way z/OS systems can share data. As the number of systems increase, it is essential to have an efficient way to share data across systems. The Coupling Facility enables centrally accessible, high-performance data sharing for authorized applications, such as subsystems and z/OS components, that are running in a sysplex. These subsystems and components then transparently extend the benefits of data sharing to their
applications. Use of the Coupling Facility substantially improves the feasibility of connecting many z/OS systems up to 32 with near linear scalability together in a sysplex to process work sharing data in parallel.
The concept of data sharing is not new. This data sharing capability follows the heritage of the mainframe’s design of share-everything architecture. Different applications within a system often need to access the same information, sometimes to read it and other times to update it. Sometimes several copies of the data exist, and with that comes the requirement of keeping all of the copies identical. If the system fails, you need a way to preserve the data with the most recent changes.
Data validity is controlled by a data management system. Within a single z/OS system, the data management system keeps track of which piece of data is being accessed or changed by which application in the system. It is the data management system’s responsibility to capture and preserve the most recent changes to the data, in case of system failure.
When two or more z/OS systems share data, each system has its own copy of a data management system. Communication between the data management systems is essential. Therefore, multisystem data sharing hinges on high-performance communication to ensure data validity among multiple data management systems, and it requires high-speed data accessing methods. Enabling the application for continuous availability gives you the opportunity to keep it running and stable even if one or more servers should become unavailable as a result of:
* Unplanned failures on one or some (but not all) of the servers
* Planned outages in the operations of one or some of the servers in connection with reconfiguration, upgrades,
maintenance
This feature of Z also provides for enhanced Total Cost of Ownership. There is little need to propagate or move data due to application locality. The Coupling Code allows for central processing of data without the concern of resource movement.
An enhancement is the System Managed Coupling Facility Duplexing which is a set of architectural extensions for Parallel Sysplex providing increase availability and access reliability for data structure redundancy.

## Slide 36: Parallel Sysplex Used for Failover (Continuous Operations)
Cloned Application
Claims
Test
Test
Under
Writing
Under
Writing
System
Image 1
System
Image 3
Appl 5
Appl 3
Under
Writing
System
Image 2
Appl 7
Workload Distributor
Appl 2
Appl 1
Appl 6
Appl 4
Appl 8
Appl 1
Appl 4
Appl 6
Shared Data
Notes: SLIDE OBJECTIVE: SET UP THE REQUIREMENT
Data Sharing
Lets look at how a shared access system works on the mainframe. We share workloads through multiple partitions and share all data through a common environment. Through the coupling facility we can share that data across multiple system images and application environments. That shared data happens because of I/O, disk devices are all shared through the integrated Channel-Architecture which has its foundation back to its original 360 design.
----- previous speaker notes -----
Connecting a large number of systems brings with it special considerations, such as how the large number of systems communicate and how they cooperate to share resources. These considerations affect the overall operation of z/OS systems. A sysplex significantly changes the way z/OS systems can share data. As the number of systems increase, it is essential to have an efficient way to share data across systems. The Coupling Facility enables centrally accessible, high-performance data sharing for authorized applications, such as subsystems and z/OS components, that are running in a sysplex. These subsystems and components then transparently extend the benefits of data sharing to their
applications. Use of the Coupling Facility substantially improves the feasibility of connecting many z/OS systems up to 32 with near linear scalability together in a sysplex to process work sharing data in parallel.
The concept of data sharing is not new. This data sharing capability follows the heritage of the mainframe’s design of share-everything architecture. Different applications within a system often need to access the same information, sometimes to read it and other times to update it. Sometimes several copies of the data exist, and with that comes the requirement of keeping all of the copies identical. If the system fails, you need a way to preserve the data with the most recent changes.
Data validity is controlled by a data management system. Within a single z/OS system, the data management system keeps track of which piece of data is being accessed or changed by which application in the system. It is the data management system’s responsibility to capture and preserve the most recent changes to the data, in case of system failure.
When two or more z/OS systems share data, each system has its own copy of a data management system. Communication between the data management systems is essential. Therefore, multisystem data sharing hinges on high-performance communication to ensure data validity among multiple data management systems, and it requires high-speed data accessing methods. Enabling the application for continuous availability gives you the opportunity to keep it running and stable even if one or more servers should become unavailable as a result of:
* Unplanned failures on one or some (but not all) of the servers
* Planned outages in the operations of one or some of the servers in connection with reconfiguration, upgrades,
maintenance
This feature of Z also provides for enhanced Total Cost of Ownership. There is little need to propagate or move data due to application locality. The Coupling Code allows for central processing of data without the concern of resource movement.
An enhancement is the System Managed Coupling Facility Duplexing which is a set of architectural extensions for Parallel Sysplex providing increase availability and access reliability for data structure redundancy.

## Slide 37: The zSeries® Parallel Sysplex Clustering Solution
Dynamic workload balancing
Continuous application availability
Incremental growth
Strategic benefits – The Ultimate
  Application availability
  Data Accessibility
  Capacity / Scalability
  Workload Management
  Single System Image
  System Management
Tactical Benefits
  IBM Software license savings
  Reduced cost of ownership
  Application scalability
  Industry direction

## Slide 38: Parallel Sysplex Software Structure

## Slide 39: Data Integrity – Cross Invalidates
LOCKS
DATA
BUFFERS
DATABASE
MANAGER
DATA
BUFFERS
DATABASE
MANAGER
Sysplex Services
Coupling Facility
REQUESTS
REQUESTS
z/OS
zSeries
z/OS
zSeries
LOCKS
Multi-System
Serialization
Changed
Data

## Slide 40: Summary
Terminology is important
The classic S/360 design is important as all later designs have enhanced it. The concepts are still relevant
New processor types are now available to reduce software costs
Clustering techniques and parallel sysplex

## Slide 41: Trademarks
DB2*
DB2 Universal Database
DirMaint
DRDA*
Enterprise Storage Server*
ESCON*
FICON*
GDPS*
HiperSockets
IBM*
The following are trademarks of the International Business Machines Corporation in the United States and/or other countries.
The following are trademarks or registered trademarks of other companies.
* All other products may be trademarks or registered trademarks of their respective companies.
Intel is a trademark of Intel Corporation in the United States, other countries, or both.
Java and all Java-related trademarks and logos are trademarks of Sun Microsystems, Inc., in the United States and other countries
Linux is a trademark of Linus Torvalds in the United States and other countries..
UNIX is a registered trademark of The Open Group in the United States and other countries.
Microsoft is a registered trademark of Microsoft Corporation in the United States and other countries.
Notes:
Performance is in Internal Throughput Rate (ITR) ratio based on measurements and projections using standard IBM benchmarks in a controlled environment. The actual throughput that any user will experience will vary depending upon considerations such as the amount of multiprogramming in the user's job stream, the I/O configuration, the storage configuration, and the workload processed. Therefore, no assurance can be given that an individual user will achieve throughput improvements equivalent to the performance ratios stated here.
IBM hardware products are manufactured from new parts, or new and serviceable used parts. Regardless, our warranty terms apply.
All customer examples cited or described in this presentation are presented as illustrations of the manner in which some customers have used IBM products and the results they may have achieved. Actual environmental costs and performance characteristics will vary depending on individual customer configurations and conditions.
This publication was produced in the United States. IBM may not offer the products, services or features discussed in this document in other countries, and the information may be subject to change without notice. Consult your local IBM business contact for information on the product or services available in your area.
All statements regarding IBM's future direction and intent are subject to change or withdrawal without notice, and represent goals and objectives only.
Information about non-IBM products is obtained from the manufacturers of those products or their published announcements. IBM has not tested those products and cannot confirm the performance, compatibility, or any other claims related to non-IBM products. Questions on the capabilities of non-IBM products should be addressed to the suppliers of those products.
Prices subject to change without notice. Contact your IBM representative or Business Partner for the most current pricing in your geography.
* Registered trademarks of IBM Corporation
IBM eServer
IBM logo*
IMS
Lotus*
MQSeries*
Parallel Sysplex*
RACF*
Rational*
System i
System z
System z9
System Storage
Tivoli*
TotalStorage*
Virtualization Engine*
VSE/ESA
VTAM*
WebSphere*
z/Architecture
z/OS*
z/VM*
z/VSE
zSeries*