## Slide 1: Chapter 19 Network Communications on z/OS

## Slide 2: AGENDA
1 - Networking history
2 – Comm server SNA and IP
3 – zSeries network adapters
4 - Sysplex networking with IP
5 - z/OS policy agent
6 - selected networking scenarios with zSeries
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3
1970
1980
1990
2000
OLD SNA
OLD TCPIP UNIX
APPN
AS400
APPN
390
EE
TCPIP
other platforms
(390)
OSI is the future
TCP/IP
is the winner
OSI is dead

## Slide 4
zSeries Networking today is :
Standardized:
Unique:
I e based on latest Ethernet and
TCP/IP technology
Offers a unique networking environment
with unmatched flexibility, availability
and performance

## Slide 5: AGENDA
1 - Networking history
2 – Comm server SNA and IP
3 – zSeries network adapters
4 - Sysplex networking with IP
5 - z/OS policy agent
6 - selected networking scenarios with zSeries
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6
Z/OS Communication Server
SNA functions are
Implemented on a
Number of platforms
Beside z/OS….
Ex: AIX, AS/400
MS Windows and
LINUX
OPEN SYSTEMS ADAPTER

## Slide 7
The origin of Systems Network Architecture (SNA)
SNA was developed and implemented in the early 1970s by IBM.
The original SNA architecture, which today is known as SNA Subarea networking, was based on a hierarchical model that matched the networking requirements of that time.
An SNA subarea network consists of three main node types:
  Hosts - mainframe operating systems such as VSE, VM, or MVS - running VTAM
  Communication controllers - specialized hardware (IBM 3705, 3720, 3725, 3745/46) and software that managed the attachment of telecommunications lines and performed the specialized processing that was needed to send/receive data over those lines
  Network devices - originally "dumb" network devices such as 3270 terminal control units (IBM 3274, 3276, 3174) to which one or up to 32 IBM 3270 terminals (IBM 3278, 3178, 3279) could be attached, but today more often workstations with one or more emulated 3270 devices
In SNA terms, those three node types were and still are known as Physical Units (PUs):
  PU Type 5: a host (a subarea node) in which a Virtual Telecommunications Access Method (VTAM) implementation with a Systems Services Control Point (SSCP) resides
  PU Type 4: (a subarea node) a communication controller in which a Network Control Program (NCP) executes
  PU Type 2.0: (a peripheral node) a terminal control unit with "dumb" devices attached or today a PC with an SNA protocol stack implemented

## Slide 8: The legacy: A traditionalSNA Network (as it was)
3745/46
3745/46
SNA
Device
SNA Device
z.B. GAA
SNA Clients
SNA APPL Gateway
TN3270 Gateway
TN3270 Clients
APPN Peer Nodes
NCP SNA
Network
Interconnect
(SNI) Nodes
NCP
Boundary
Nodes
Token Ring
IP or SNA
Network
APPN
network
SNA
Network
X.25
QLLC
IP
Network
Bank ABC
Business partner

## Slide 9
APPN is part of the SNA architecture - an extension to the base subarea SNA architecture
In an APPN network, nodes are peers - there is no hierarchical relationship between nodes
An SNA network may consist of both subarea and APPN nodes
  Some nodes may be both a subarea node and an APPN node
Main characteristics of an APPN network are:
  LUs can be found dynamically anywhere in the APPN network
    Directory Services
  Route selection is done dynamically and includes dynamic changes to the network topology
    Topology and Routing Services (TRS)
  Provides intermediate session routing
    Traffic between two nodes may pass through one or more intermediate APPN nodes
  Reduces system definition
    Logical units and control points need be defined only on owning node
    Routes dynamically determined at session setup time
The typical LU type in an APPN network is an LU Type 6.2
  Adjacent dependent LUs are supported by some APPN nodes (such as VTAM) that support optional APPN extensions that are known as Session Services Extensions (SSE)
  Non-subarea adjacent dependent LUs can route through an APPN network using a technology that is known as Dependent LU Requester (DLUR) and Dependent LU Server (DLUS)
What is Advanced Peer to Peer Networking (APPN)?

## Slide 10
APPN multiple network connectivity
EBN
EN
EN
EN
APPN Network ID: NETA
EN
EN
NN
EBN
EN
EN
EN
NN
EBN
EN
EN
EN
NN
EN
EN
EN
NN
EBN
EN
EN
EN
NN
EBN
APPN Network ID: NETB
APPN Network ID: NETC
APPN Network ID: NETD
Extended Border Nodes (EBNs) are extensions to the base APPN function
  Limit topology exchange
  Allow directory flows (searches)
Used when connected NNs have different NET IDs
  native net refers to the NET ID a node belongs to
  non-native net refers to nodes with different NET IDs
Searching can be entirely dynamic or controlled via system definitions
If EE is used between EBNs, the physical connectivity between different networks (business partners) may be via an IP network

## Slide 11
What about my SNA applications?
Most mainframe installations still have a mainframe SNA application portfolio to support and to provide access to:
  An SNA application either uses SNA programming interfaces directly or relies on its underlying middleware, such as CICS or IMS, to use SNA programming interfaces on its behalf
  More recent application subsystems are either network programming interface agnostic or are based on IP network programming interfaces - such as sockets
  Most mainframe installations today have a mix of application subsystems, where some require SNA networking technologies and some require IP networking technologies
The branch and regional offices are increasingly moving towards IP-based client platforms, of which the ultimate is the universal client interface - a Web browser:
  The IP-based client platforms need access to both newer IP-based services in the data center and to older SNA-based services
  To access SNA-based mainframe applications from such IP-based client interfaces, one or more gateways that transform between different networking- and application protocols are needed somewhere in-between the client platform and the mainframe
  That's where SNA/IP integration technologies come into the picture!
How can I continue to provide access to my SNA-based mainframe applications, while at the same time expanding my IP-based mainframe application portfolio?

## Slide 12
IBM 3270 SNA application access evolution
3270
VTAM
SNA 3270 Application
VTAM
SNA 3270 Application
VTAM
SNA 3270 Application
VTAM
SNA 3270 Application
VTAM
SNA 3270 Application
3270
Coax
SDLC serial line
NCP
NCP
SDLC serial line
3270
LAN with IP
3270
Item 1
Item 2
TN3270 Server
WebSphere Application Server with HATS
HOD Server
TN3270 Server
TN3270 Server
IBM 327x terminal
PC with SNA 3270 emulation
PC with TN3270 emulation software pre-installed (PCOM)
PC with Web browser and on-demand TN3270 emulation software (HOD)
PC with Web browser
LAN with IP
LAN with IP
SNA
SNA
SNA
SNA
SNA
TN3270/IP
TN3270/IP
TN3270/IP
HTTP(S)/IP
LAN with SNA
Coax
No change was ever required to the mainframe SNA application!
HTTP(S)/IP
End user interface transformation rules and logic

## Slide 13
Premier SNA/IP integration technology: Enterprise Extender
EE offers a one-stop solution for SNA/IP integration that supports both branch and business partner communication and offers the opportunity for use of IP network flows end-to-end
Use of EE requires no changes to SNA applications
Network infrastructure is native IP, which allows the router infrastructure to maximize router efficiency - no need for routers to perform functions beyond native IP routing
Use of EE can reduce the APPN network complexity by collapsing the APPN Network Node (NN) topology into the data center
  Minimizes the effect of APPN network searches
EE can be used to implement business partner communication based on the APPN Extended Border Node (EBN) function
  SNA over IP end-to-end with z/OS business partners
ANR/EE
Application
RTP
IP
DLC
API
IP
Network
Application
RTP
IP
DLC
API
RTP
ANR
DLC
API
Appl
ANR/EE
EE Link
RTP Connection/Pipe
Session Partners
HPR Link
So - why don't all z/OS installations use EE on z/OS?
  Requires APPN and HPR enablement of the z/OS environment
  EE uses UDP packets and that causes problems for firewall administrators
  EE requires coordinated actions by both end-points
    Issue for business-to-business communication
    Not all business partners are able to make similar changes

## Slide 14: Enterprise extender Network Scenario

## Slide 15: AGENDA
1 - Networking history
2 – Comm server SNA and IP
3 – zSeries network adapters
4 - Sysplex networking with IP
5 - z/OS policy agent
6 - selected networking scenarios with zSeries
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: z900/z990 Network adapters
zSeries
OSA
OSA
z/VM
zLinux2
zLinux3
z/OS C
TCP/IP
Stack
zLinux1
z/OS A
z/OS B
HIPERSOCKETS
Guest LAN & virtual Switch

## Slide 17: z900/z990 Hipersockets - Sample
zSeries
OSA1
OSA2
z/VM
zLinux2
zLinux3
z/OS C
HiperSockets
TCP/IP
Stack
Campus
Network
IP Net A
IP Net B
zLinux1
z/OS A
z/OS B

## Slide 18: AGENDA
1 - Networking history
2 – Comm server SNA and IP
3 – zSeries network adapters
4 - Sysplex networking with IP
5 - z/OS policy agent
6 - selected networking scenarios with zSeries
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Dynamic VIPA – Sysplex Distributor Function - 1
Use of Sysplex Distributors enables load balancing and transparent failover
  One Distribution z/OS System
  Two or more Application z/OS Systems
  One Backup Distribution System (Optional)
  All Systems have direct network access over OSA adapter
  All systems connected with sysplex XCF
Startup:
  The Distribtor activates the dyn. VIPA Address and the Destination Port Table (DPT)
  The Applications are started on the Application Systemens and registers with Workloadmanager.
  The WLM (Work Load Manager) informs the distributor about target applications
  The dyn. VIPA Address is active on Distributor and on the Appl. Systems but is only announced (OSPF) by the Distributor
SYSC
OSA1
Appl-A
IP-V
OSA2
SYSD
OSA1
Appl-A
IP-V
OSA2
SYSE
OSA1
Appl-A
IP-V
OSA2
Distributor
DPT:
OSA1
IP-V
OSA2
Backup-D.
DPT:
OSA1
IP-V
OSA2
XCF
Campus
Network
Dyn. Routing
WLM

## Slide 20: Dynamic VIPA – Sysplex Distributor Function - 2
Campus
Network
Normal operation:
  Session Request from Client to Appl-A
  On the TCP-SYN Packet the Dist. System selects an Appl. System. Selection is based on WLM data.
  Info about the session is entered in the DPT
  The packet is forwarded to the target (Application-) system over XCF
  The Application System answers directly over its OSA adapter
  Using the entries in the DPT all following packets in this TCP Session are forwarded to the same target system
  All TCP Sessions are, depending on the load situation distributed among the Application Systems
SYSC
OSA1
Appl-A
IP-V
OSA2
SYSD
OSA1
Appl-A
IP-V
OSA2
SYSE
OSA1
Appl-A
IP-V
OSA2
OSA1
OSA2
XCF
Distributor
DPT:
Pt.1 -> SYSC
Pt.2 -> SYSE
IP-V
Backup-D.
DPT:
Pt.1 -> SYSC
Pt.2 -> SYSE
OSA1
IP-V
OSA2

## Slide 21: Dynamic VIPA – Sysplex Distributor Backup scenario 1
Campus
Network
Failure of an Application Server
  SYSC is, planned or unplanned, taken down.
  The existing TCP Sessions to SYSC are interrupted
  Over WLM/XCF the Distributor is informed that SYSC is lost deletes all entries with SYSC from the DPT
  All new TCP Sessions are distributed among the remaining systems (SYSE and SYSD)
SYSC
OSA1
Appl-A
IP-V
OSA2
SYSD
OSA1
Appl-A
IP-V
OSA2
SYSE
OSA1
Appl-A
IP-V
OSA2
OSA1
OSA2
XCF
Distributor
DPT:
Pt.1 -> SYSC
Pt.2 -> SYSE
OSA1
OSA2
DPT:
Pt.3 -> SYSD
Pt.2 -> SYSE
WLM
IP-V
Backup-D.
DPT:
Pt.3 -> SYSD
Pt.2 -> SYSE
IP-V

## Slide 22: Dynamic VIPA – Sysplex Distributor Backup scenario 2
Campus
Network
Failure of the Distributor
  The distributor system is, planned or unplanned, taken down
  Over XCF communication the Backup Distributor is informed
  The Backup Distributor activates the dyn. VIPA Address and announces the VIPA with OSPF
  The DPT is in normal operation mirrored from the active distributor and is now activated
  All existing TCP-Sessions are immediately rerouted through the Backup Distributor. The traffic is uninterrupted.
SYSC
OSA1
Appl-A
IP-V
OSA2
SYSD
OSA1
Appl-A
IP-V
OSA2
SYSE
OSA1
Appl-A
IP-V
OSA2
OSA1
OSA2
XCF
Distributor
DPT:
Pt.1 -> SYSC
Pt.2 -> SYSE
OSA1
OSA2
IP-V
Backup-D.
DPT:
Pt.1 -> SYSC
Pt.2 -> SYSE
IP-V
DPT:
Pt.1 -> SYSC
Pt.2 -> SYSE
IP-V
Dyn. Routing
-> z/OS V1R5

## Slide 23: AGENDA
1 - Networking history
2 – Comm server SNA and IP
3 – zSeries network adapters
4 - Sysplex networking with IP
5 - z/OS policy agent
6 - selected networking scenarios with zSeries
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24
Policies Managed by the Policy Agent on z/OS
Network Quality of Service policies
  Differentiated services (prioritization of IP packets)
  Sysplex Distributor Policies Source based input to SD decision process
Intrusion Detection Services policies
  Scans
  Attacks
  Flooding (traffic regulation)
IPSec and AT-TLS (from z/OS 1.7)
Routing policies

## Slide 25
Applications, Users, Time-of-Day - and IP Network Service
TN3270 Traffic for
Customer Query Dept.
from 8AM to 5PM
FTP Traffic
for all
User Group One
(Customer Query Dept.)
User Group Two
(Bookkeeping Dept.)
User Group Three
(IT Dept.)
TN3270 Traffic for
Bookkeeping Dept.
We need the ability to classify traffic by application, user group, and time of day - and assign relative priority to such traffic.

## Slide 26
Secure access to both TCP/IP and SNA applications
Focus on end-to-end security and self-protection
Exploits strengths of S/390 and z900 HW and SW
z/OS
Secure protocols
(IPSec, SSL, SNA SLE)
with Strong 3DES Encryption
RACF for
  User I&A
  Access Ctl
Mission-critical data
Secure Key Distribution
Enterprise Network
or Intranet
Internet
F
I
R
E
W
A
L
L
Enterprise Network
or Intranet
F
I
R
E
W
A
L
L
Security Server
Communications Server
IBM
IBM
IBM
IBM
IBM
Intranet Host
Remote Access
Business Partner
Network IDS
z/OS CS IDS
Application level security
  Base is platform security
  SSL for TN3270E and Web
  SSL for FTP (z/OS V1R2)
  Kerberos (z/OS V1R2)
  Client authentication based on digital certificates
Network level security
  VPN IPSec and IKE with Security Server
  Intrusion detection
Universal Access to Business Data Without Universal Exposure

## Slide 27
IPSecurity Overview – IP Packet Filtering
Filter rules defined to match packets based on:
  Packet information
  Network attributes
  Time
Used to control:
  Traffic being routed
  Access at destination host
Possible actions:
  Permit
  Deny
  Permit with manual IPSEC
  Permit with dynamic IPSEC
  Log
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28
Intrusion Detection Policies
Information Gathering
  Network and system topology
  Data location and contents
Unauthorized Usage
  Eavesdropping/Impersonation/Theft
    On the network/on the host
  Base for further attacks on others
    Amplifier
    Robot or zombie
Denial of Service
  Attack on availability
    Single Packet attacks - exploits system or application vulnerability
    Multi-Packet attacks - floods systems to exclude useful work
    Firewall can provide some level of protection from Internet
Perimeter Security Strategy alone may not be sufficient. Consider:
  Access permitted from Internet
  Trust of intranet
    Users
    Ability of servers to withstand being taken over
      Amplifiers, Robots, zombies
Enterprise Network
or Intranet
Internet
Attacker
End User
Attacker
Firewall
Server
Zombie
Attackers
Intrusions can occur from Internet or intranet

## Slide 29: AGENDA
1 - Networking history
2 – Comm server SNA and IP
3 – zSeries network adapters
4 - Sysplex networking with IP
5 - z/OS policy agent
6 - selected networking scenarios with zSeries
dis
disclaimer:
The scenarios on the following pages does not show actual installations. They are only children of my imagination to show infrastructures that can be bult using networking technologies available in zSeries.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30
olle.zetterlund@se.ibm.com
LSU Nordics 2004
"IP Infrastructure network"
Internet
Firewall(s)
LDAP server
Authentication
Open web servers
DNS servers
Proxy(s)
SSL termination
Router(s)
Switch(es)
.....
DMZ

## Slide 31
olle.zetterlund@se.ibm.com
LSU Nordics 2004
build dmz in the box
Internet
Linux
dmz

## Slide 32
build dmz in the box
Internet
O
S
A
e
x
p
r
Stonegate
Firewall
Tivoli
policy
director
LDAP
server
Tivoli Access
Manager
(webseal)
Linux web
server
Firewall(s)
LDAP server
Authentication
Open web servers
Proxy(s)
SSL termination
Router(s)
Switch(es)
Stonegate
Firewall

## Slide 33
build dmz in the box II
Internet
O
S
A
e
x
p
r
Stonegate
Firewall
LDAP
server
Linux web
server
Firewall(s)
LDAP server
(Authentication)
Open web servers
Proxy(s)
SSL termination
Load distribution
Router(s)
Switch(es)
HTTP Server
with
websphere plugin
Sysplex
Distributor
Linux web
server

## Slide 34
O
S
A
e
x
p
r
Stonegate
Firewall
LDAP
server
Linux web
server
HTTP Server
with
websphere plugin
Stdby
sysplex
distributor
O
S
A
e
x
p
r
Stonegate
Firewall
LDAP
server
Linux web
server
HTTP Server
with
websphere plugin
Sysplex
Distributor
coupling
facility
All-in-z Sysplex
external
load balancer
e g
ND
or
Cisco
R
O
U
T
E
R
Internet
ISP1
Internet
ISP2

## Slide 35
T h e E n d