IBM Intelligent Cluster factory settings

November, 2014
# The following tables show the factory settings for network addressing, user IDs, rack numbering, BladeCenter® / Flex / NeXtScale unit and node numbering, I/O bay location numbering, and hostnames of the various IBM® Intelligent Cluster ™ components. Table 6 lists the factory set hardware user ID and passwords.
## Table 1: Network addressing* and host names

IP Address	Hostname	Component
172.20.0.1	mgt.cluster.com	Management node eth0 (cluster vlan)
172.30.0.1	mgt1.cluster.com	Management node eth1 (management vlan)
172.29.0.1	bmc	Management node alias eth0:1 (cluster vlan )
172.29.101.1*	bmc001	Node BMCs
172.30.1.1	storage001	Storage nodes
172.30.2.1*	triton01A	DS3000/DS3500, V3700, v7000 storage controllers (A, B)

172.30.3.1	RamSan	IBM FlashSystem 720. 820
172.30.4.1	GSS x (1 or 2)	GSS Storage Server (Two servers in each solution)
172.20.101.1	node001	Compute nodes
172.40.101.1	hca001	HCA cards ib0 (cluster vlan)
172.20.4.1	user001	User nodes
172.30.10.1*	ql-001 / mlnxsx6036-001 / mlnxsx6036-001 / mlnxsc6512-001 / mlnxsc6518-001 / mlnxsx6536-001 / mlnxsx6536-001	InfiniBand Switches / Qlogic 12200, 12800 / Mellanox SX6036 FDR-10 (SB) / Mellanox SX6036 FDR14 / Mellanox SX6512 FDR14 / Mellanox SX6518 FDR14 / Mellanox SX6536 FDR-10 (SB) / Mellanox SX6536 FDR14
172.30.15.1*	mlnxsx6036-GW-001	IB to Eth Gateway / Mellanox SX6036-GW IB to Eth Gateway
172.30.20.1*	ts-001	Terminal servers : Cyclades ACS32/ACS48
172.30.50.1*	bnt80xx-001 / ibm8052-001 / ibmG7028 / lge4550-001 / lge5048xg-001 / lgees4052g-001 / smc8126-001 / smc8150-001 / ecs4110-52T -001 / ecs4510-52T -001 ecs4600-54T -001 / extX460-48T -001	1U/2U 1G Ethernet Switches / BNT G8000 / IBM BNT G8052 / IBM RackSwitch G7028 / LG-Ericsson 4550G (SB) / LG-Ericsson ES-5048XG (SB) / LG-Ericsson ES-4052G / SMC 8126L2 (LG-Ericsson) (SB) / SMC 8150L2 (LG-Ericsson) (SB) / Edge-Core ECS4110-52T 1GbE Switch / Edge-Core ECS4510-52T 1GbE Switch / Edge-Core 4600-54T 1GbE Switch Extreme Summit X460-G2-48t 1GbE Switch
172.30.55.1	ibm8264-001 / ibm8316-001 / ibm8332-001 / mlnxsx1036-001 / ecs5610-52S-001 ecs5600-52X-001 / ecs6700-32X-001 extX670-48x -001 / extX670-48t -001 / extX770-32q -001	1U/2U 10G / 40G Ethernet Switches / IBM BNT G8264 / IBM RackSwitch G8316 / IBM RackSwitch G8332 / Mellanox SX1036 40GbE / Edge-Core ECS5610-52S 10GbE Switch / Edge-Core 5600-52X 10GbE Switch / Edge-Core 6700-32X 40GbE Switch / Extreme Summit X670V-48x 10Gb Switch / Extreme Summit X670V-48t 10Gb Switch / Extreme Summit X770-32q 40GbE Switch
172.30.60.1*	apc-001	APC
172.30.65.1*	lsisas6160-001	LSI SAS6160 SAS Switch
172.30.70.1*	rcm-001	RCM
172.30.80.1*		Enterprise Ethernet Switches
172.30.85.1*	fc-001	Fibre Channel switches
172.30.101.131*	mm-001	BladeCenter AMM / Flex CMM / FeiHu FPM

Indicates the hard-coded IP address of the various Intelligent Cluster components.
## Note: IP addresses for similar components increment based on location from the bottom upward and from
## left to right within the rack (as viewed from the front), and then continue from left to right across the racks
## of a multi-rack solution.
## Table 2: Compute node IP addressing

Rack name	Network	Rack number	Node*
Rack1	172.20	101	1 to 112
Rack2	172.20	102	1 to 112

Example: rack 1, node 1 = 172.20.101.1
* Node numbering increases from the bottom of the rack upward.
BladeCenter / Flex / Fei Hu node numbering increases from the bottom of the rack upward, and from left to
right within the BC chassis, or within same U location in Flex /FeiHu chassis.
## Table 3: BMC IP addressing

Rack name	Network	Rack number	Node
Rack1	172.29	101	1 to 112
Rack2	172.29	102	1 to 112

Example: rack 1, node 1 = 172.29.101.1

## Table 4: BladeCenter module IP Addressing BC-H with advanced management module (AMM).
Flex CMM and Fei Hu FPC module IP addressing follows same strategy as BC AMM.

Network	Rack number	I/O bay location number (1-10) + BladeCenter unit number (1-6)
172.30*	101	1 to 10 (SM I/O bay 1 – SM I/O bay 10) + 1 to 6 BC / Flex chassis
172.30*	102	1 to 10 (SM I/O bay 1 – SM I/O bay 10) + 1 to 6 BC / Flex chassis
172.30*	101	AMM* / FPC 130 + 1 to 6 BC or Fei Hu chassis number / CMM ** 130 + 1 to 6 (1 st CMM in chassis up to 6) / 2nd CMM in chassis 140 + 1 to 6 (2nd CMM in chassis up to 6) / *all AMMs in the same BladeCenter share one IP address. / ** Each CMMs must have a unique IP address see example below.

Examples: 172.30.101.34 – the switch module fitted to I/O bay 3 in BladeCenter unit 4 of rack 1
172.30.102.46 – the switch module fitted to I/O bay 4 in BladeCenter unit 6 of rack 2
172.30.106.104 – the switch module fitted to I/O bay 10 in BladeCenter unit 4 of rack 6
172.30.106.133 – the AMM for BladeCenter unit 3 of rack 6
Example (FLEX CMM)
172.30.101.131 1st CMM in a chassis
172.30.101.141 2nd CMM in SAME chassis as 1st CMM

## Table 5: InfiniBand HCA IP Addressing

Rack name	Network	Rack number	HCA*
Rack1	172.40	101	1 to 112
Rack2	172.40	102	1 to 112

Example: rack 1, hca 1 = 172.40.101.1

*Host channel adapter (HCA) numbering increases from the bottom of the rack upward.
# Table 6: Factory set user IDs and passwords

Hardware	User ID	Password	Comments
Avocent MP 5300	root	avocent	Default
APC switch	apc	apc	Default
Itouch terminal	access	system	Default
InReach terminal	InReach	access	Default
BNT switch	admin	admin	Default
Cyclades terminal	root	tslinux	Default
Cisco switch	(see Comments)	ibm1350	Press Enter at the userid prompt
LG-Ericsson 4550, 5048, 4052	admin	admin	Default
LSI SAS6160	admin	admin	Default
SMC switch	admin	admin	Default
SMC 8024L2	admin	smcadmin	Default
DS3000/4000 Storage	shellUser	wy3oo&w4	Default
Fibre Channel switch	admin	password	Default
FlashSystem 7010/20, 810/20	admin	password	Default
Force10	none	none	For priv exec, the password is force10
RSAs	USERID	PASSW0RD	The 0 in passw0rd is a zero
Flex CMM	USERID	Passw0rd	The 0 in passw0rd is a zero
BladeCenter AMM / FeiHu FPM	USERID	PASSW0RD	The 0 in passw0rd is a zero
Cisco InfiniBand switch	admin	adminpass	Default
Mellanox	admin	admin	Default
Qlogic InfiniBand switch	admin	adminpass	Default
V3700 / V7000	superuser	passw0rd	Default
Voltaire InfiniBand switch	admin	123456	Default
QLogic BC FC switch module	USERID	PASSW0RD	The 0 in passw0rd is a zero
Juniper	admin	admin	Create at initial log in
Edge-Core	admin	none	Default

## Table 7: Operating system passwords
Operating system	USERID	Password
Management server	root	ibm1350
Nodes	admin / root	cluster / cluster

_________________________

IBM, BladeCenter and Intelligent Cluster are trademarks of the IBM Corp. in the United States, other countries, or both. Other company, product, or service names may be trademarks or service names of others.

©Copyright International Business Machines Corporation 2007. All rights reserved.
US Government Users Restricted Rights – Use, duplication or disclosures restricted by GSA ADP Schedule Contract with IBM Corp.